## Slide 1: FAT Filesystem

## Slide 2: Agenda
Introduction and History
Disk Structures and Partitions
FAT file system structure
Long File Names
Embedded FAT tips and tricks
File Recovery
Common Problems
Useful Tools

## Slide 3: Introduction and History
Developed by Bill Gates and Marc McDonald in 1976-1977
Named from table which holds the information which stores used and/or free space information
Originally was FAT12, then FAT16 and now FAT32.

## Slide 4: Disk Structure
Disks can often have multiple partitions
Each partition can have different file system
Master boot record describes the primary partition
SD cards and Flash drive may not have MBR
MBR
Partition 1
Partition 2

## Slide 5: FAT Partition Map
Boot Sector is also known as BIOS Parameter Block
There maybe be two copies of FAT table in case one get corrupt
Data is where file data is stored
Boot
Sector
FS Info
(FAT32)
Reserved
Sectors
FAT #1
FAT #2
Root Directory (FAT12 FAT16)
Data

## Slide 6: What is a Sector
A sector is a block of data, usually 512 bytes.
SD cards and most flash drives are sector base devices. That is you can only write a sector at time.

## Slide 7: Boot Sector (FAT12/FAT16)
Not the first sector on drive if drive has MBR, however on Flash drives and SD cards it usually is.
Contains key information including:
  Bytes per Sector
  Sectors per Clusters
  Reserved sectors
  Number of FATs
  Maximum root directory entries (FAT12 FAT16)
  Total Sectors
  Sectors per FAT (2 bytes)
  Boot Code
  etc

## Slide 8: Boot Sector (FAT32)
FAT32 added some additional data in boot sector
  Sectors per FAT (4 bytes)
  Cluster number for Root Directory (4 bytes)
  FS Info Sector (2 bytes)
  Sector for copy of boot sector (0 if none)
  etc

## Slide 9: FS Information Sector
This section is optional in FAT32, not all OS uses it. Not used on FAT12/FAT16
Was added for speeding up access times
  Number free clusters (-1 if unknown)
  Last used cluster

## Slide 10: Definition: Cluster
A cluster is a block of contiguous sectors
In Boot Sector it might indicate that a cluster is 2 sectors, can be (1-128). Thus if sector is 512 bytes then a cluster in this example is 1024 bytes.
Data section is a collection of clusters

## Slide 11: File Allocation Table
For every cluster in the data section there is a FAT entry.
The FAT entry is 12, 16, or 32 bits depending on FAT12, FAT16, or FAT32.
The entry in the FAT table creates a linked list to represent clusters used on a file, with following special flags:
  0 is a free cluster (not allocated to file)
  1 reserved cluster (not to be used)
  0xFFF0-0xFFF6 reserved (not FAT12 nominclature)
  0xFFF7 bad sector on disk
  0xFFF8-0xFFFF last sector in chain (End Of Chain –EOC)

## Slide 12: FAT Example
3
4
0xFF8
0
0
0
2
3
4
5
6
n
USED
FAT
Clusters
USED
USED
2
1
0
3
FREE
FREE
FREE
4
n-2

## Slide 13: Directory Table
The directory table links a file name, or directory, to a cluster chain in FAT.
Basic information in a directory entry are:
  File name and extension
  File Attributes
  Time stamps
  File Size in bytes
  First cluster in file

## Slide 14: File Example
text.txt
File Name
10
Size (Bytes)
2
First Cluster
3
4
0xFF8
0
0
0
2
3
4
5
6
n
USED
FAT
Clusters
USED
USED
2
1
0
3
FREE
FREE
FREE
4
n-2
Directory Entry

## Slide 15: File Example Continued
Assume cluster size is 1024 bytes
In previous example what is size of file on disk?
How many bytes on disk are used?
Hence a file can be no smaller than one cluster.

## Slide 16: What is a Directory?
A directory and a file are basically the same in FAT, both are just entries in Directory Table.
A directory has the file attribute set to indicate a directory.
The “directory file” contains a Directory Table, thus a sub directory is a file that contains Directory Table entries.

## Slide 17: Root Directory
FAT12 and FAT16 reserved clusters for root directory
This limited maximum number of root directory entries.
FAT32 fixed this and allows the size of root directory to grow, just like any other file.
Boot
Sector
FS Info
(FAT32)
Reserved
Sectors
FAT #1
FAT #2
Root Directory (FAT12 FAT16)
Data

## Slide 18: Fragmentation
0xFF8
10
Free
FREE
0
0
text.txt
File Name
1200
Size (Bytes)
2
First Cluster
4
0xFF8
0xFF8
0
0
0
2
3
4
5
6
n
USED
FAT
Clusters
USED
USED
2
1
0
3
FREE
FREE
FREE
4
n-2
Directory Entry
bob.txt
File Name
11
Size (Bytes)
3
First Cluster

## Slide 19: Long File Names
To do long file names and remain backwards compatibility with 8.3 file naming convention in dos Microsoft used multiple directory entries to do this:
  File Attribute became 0x0F (invalid entry for DOS)
  They change directory entry to provide 22 additional name characters, plus a sequence number.
  Sequence number ORed with 0x40 for first entry (last part of name). See example next.
  Additional entries for checksum, to verify long filename truly matches a file.

## Slide 20: Long File Name Example
The following is a set of entries for long file name:
Sequence | Entry Data | Attribute Flags
0x43 | “me.ext” | 0x0F
0x02 | “y long filena” | 0x0F
0x01 | “File with ver” | 0x0F
???? | Normal 8.3 entry | Normal Flags

## Slide 21: FSCK (Check Disk for Andy)
FSCK on a FAT formatted drive does a few things:
  Checks duplicate FAT tables for errors
  Checks for FAT entries which are not connected to a file.
  Checks for Files where size is greater than number of clusters allocated to file.
  May remove extra allocated clusters to files, ie clusters that are bigger than file size.

## Slide 22: File Recovery
If your wife is like mine, at some point she will delete pictures from SD card before saving them. Under linux use “recoverjpeg” here is how it works.
  First jpegs have a nice header. Thus search for header once found assume file is store contigous.
  This works because on camera files are opened and saved one at a time, thus will usually not be fragmented.
  Deletes and format usually does not zero out clusters, just zeros FAT table and root directory table.

## Slide 23: Embedded Gotchas
When working with FAT here are some embedded gotchas.
  As you write data you have to update the size of the file in the directory structure. This causes constant rewrites to same sector in memory. Most flash and SD cards have controllers to do wear leveling these days but it is still a performance bottle neck.
  Directory table has access time stamp, if you want to update it.

## Slide 24: Embedded Tricks and Speed Boosts
If you are allocating a file, you can pre-allocate more clusters than you need.
Store the last FAT location, see the FS Info structure.
  Thus if you allocate more space you can quickly jump to where last free cluster was in FAT table.
You may choose to use one FAT table for performance boost

## Slide 25: SD Card Performance
SD cards have built in controllers for doing wear leveling. Thus writing a sector of data is normally fast but can appear to be randomly slow. Some tricks are:
  Pre erase sectors
  Do multi-block writes
  Have large buffer to hold data when writes are slow, mainly for streaming devices.

## Slide 26: Flash Problems
Most flash memories are set to all ones (0xFF) when erased. Microsoft when doing a full format of a device likes to zero out all the clusters, just opposite of what you want…
  Not sure if controllers on SD cards ignore this or not.

## Slide 27: Common Problems
Limit of ~50 files
  A directory entry is 32 bytes thus 32*50=1600. Most likely limit is really 48 if cluster size is three 512 byte clusters.
  Reason is that in FAT32 the root directory after format is allocated as one cluster. Thus if cluster is three sectors it will fill after 48 entries and then file system drive needs to allocate new cluster to extend root directory.

## Slide 28: Common Problems
Is it FAT12, FAT16 or FAT32?
  In the Boot Sector there is text for file system type, this should be ignored.
  File system is FAT12 if number of clusters is less than 4085.
  File system is FAT16 if number of clusters is greater than 4084 and less than 65525.
  If over 65524 then it is FAT32.
  Coders are often off by 1 on the above comparison, thus best to not format file system with cluster count anywhere close to these numbers.

## Slide 29: Common Problems
File Deletion
  A file is marked for deletion if first character in file name is 0xE5. This means the file is not actually deleted from disk but marked as such.
  This can create problem where file is deleted but space does not appear to be reclaimed.

## Slide 30: Common Problems
FAT indexing starts with 2.
  This is because 0 and 1 are used as flags. Thus cluster number verse FAT index number often causes problems in file system.

## Slide 31: Common Problems
File name errors
  If file name has 0xE5 as first character the it could be a problem. Thus if file name starts with 0xE5 it should be preceded with 0x05
  Normal problems with “.” and “..” file names. When a directory is created then the “.” and “..” entries in that directory table should also be created.
  Capitalization, use capitol letters! NT and latter OSs added flag to directory structure to determine if the name and/or extension should be lower case or not. FAT however does not support mixed cases.

## Slide 32: Useful Tools and References
dd – DD is the most useful tool you will find!
Dosfstools – look at the source especially fsck
EFSL – hey it is free, quit bitching.
Wikipedia – has great documentation for FAT
Microsoft – freely publishes FAT32 file system specification documentation.
Recoverjpeg – “Dear I deleted the SD card before I downloaded the pictures. Here go get my pictures back.” “But dear you deleted them!” “Oh shut-up and go do it!”