## Slide 1: Introduction to C programming
There are 10 type of people in the world, those that understand binary and those that don’t.

## Slide 2: A Basic Computer
First we will design a basic computer that can do basic operations.
Register files
Instruction decoder
Example instructions

## Slide 3: Binary and Hex
Computers speak binary which is also known as base 2. Humans normally speak base 10.
To count in binary you have
  0000 - 0
  0001 – 1
  0010 - 2
  0011 – 3
  0100 – 4
  0101 – 5
  0110 - 6
  0111 - 7
  1000 - 8
  1001 – 9
  1010 - 10 (A)
  1011 – 11 (B)
  1100 – 12 (C)
  1101 – 13 (D)
  1110 – 14 (E)
  1111 – 15 (F)

## Slide 4: Binary and Hex
To make binary easier we often count in hex, base 16.
To indicate hex number we will prefix with 0x
  0000 - 0
  0001 – 1
  0010 - 2
  0011 – 3
  0100 – 4
  0101 – 5
  0110 - 6
  0111 - 7
  1000 - 8
  1001 – 9
  1010 - 10 (A)
  1011 – 11 (B)
  1100 – 12 (C)
  1101 – 13 (D)
  1110 – 14 (E)
  1111 – 15 (F)

## Slide 5: Hex Examples
0x03 – 3
0x0F -15
0x10 – 16
Note that each character in hex number is four bits. Thus two digits above make 8 bits.

## Slide 6: Registers
Registers or “register file” is some memory that the processor can get and store data from.
For our processor we will assume we have 16 registers
8-bit wide registers

## Slide 7: Instructions
General instruction format is
Since we have 15 registers each source and destination fields are 4 bits each.
Thus last two blocks in instruction takes 8bits
We will assume the instruction is 16 bit wide
This leaves 8 bits for operation, hence we can have 256 instructions on our processor

## Slide 8: Instructions example
NOP – no operation 0x0000 or 0xFFFF (why?)
Add – 0x01xx
  So lets say you want to add value in R0 to R1 and store results back in R0. Then your instruction to do this would be 0x0110
LOAD Immediate – 0x800x then we will assume the next 16 bits contain the data to load. So to load 3 into R1 we would send computer two 16 bit numbers: 0x8001 0x0003.

## Slide 9: A Simple program
Load R1 with 3
  0x8001
  0x0003
Load R0 with 4
  0x8000
  0x0004
Add R0 to R1 and store in R0
  0x0110
Now R0 contains 7

## Slide 10: Assembly
Assembly is a programming language for a processor.
Thus for our simple example in previous slide the Assembly might be:
  LD R1,3
  LD R0,4
  ADD R0,R1
An assembler will convert these commands to our machine instructions:
  0x8001
  0x0003
  0x8000
  0x0004
  0x0110

## Slide 11: New Instructions
In last example we waste a lot of bits with our load, specifically the second 16bits we send we only used 8 bits.
So lets make a new load instruction 0x810x which loads 16bits into an even and odd registers.
0x8100 0x1234 would load R1 with 0x12 and R0 with 0x34.

## Slide 12: Programming Language Levels
Machine Code
Assembly – one to one size and speed to machine code
C programming
Compiled languages (C++, pascal, fortran, etc)
Interpoted languages (C#, JAVA, Python, etc)

## Slide 13: Language Costs and Benifits
As you move higher up in the programming language abstraction level, your development time decreases.
As you move higher up in the language your execution speed and code size increases.
Note you can write bad code in any language!

## Slide 14: What is C
C is a programming language invented by Dennis Ritchie between 1969 and 1973.
Designed to be make assembly programming easier.
Usually has 2-4x cost over assembly (size and speed)

## Slide 15: Why C
Efficient to for processor and programmer
Easy to learn, only ~33 reserved words
  auto else long switch break enum register typedef case extern return union char float short unsigned const for signed void continue goto sizeof volatile default if static while do int struct _Packed double
Code is more portable than assembly

## Slide 16: C Example
Adding our two numbers
void main(void)
{
uint8_t i,j;
i=3;
j=4;
i=i+j;
}

## Slide 17: Programming
Program starts at a function called main()
Code executes from top down
Expressions evaluated right to left (normally)
There are as many exceptions to rules in C as there are rules.

## Slide 18: Programming Examples
Continue with Programming examples
  If statements
  Function calls and return
  Printf
  Operators