## Slide 1: Embedded Class 9
Pin Driver

## Slide 2: Agenda
Requirements for Driver
Implementation Detail
Discussions

## Slide 3: Requirements
Correct Code
  This is always a requirement
Understandable Code
  This is always a requirement
Abstraction
  abstract pin such that pin assignments can change
  pin requires no changes in code.
Fast code
  Ideally one or two assembly instructions to set GPIO high/low
Low memory usage
  Should use minimal RAM
Minimal Dependencies
  Should use minimal libraries/code as it is part of our foundation’

## Slide 4: Attributes
What information do we need for a pin?
  Port and pin number
  Which mux it uses
  Which peripheral uses it.
  State for sleeping
  Others?

## Slide 5: Structure
Structs (aka structures)
  Group of related information or attributes together
typedef struct {
uint32_t pinNum;
void *ptrPeriheral;
pinMuxType_t type;
uint32_t param; //pad pin waveform
pinMuxType_t sleepType;
}pin_t;

## Slide 6: Typedef
Create a new data type in C/C++
typedef enum {
PERPIHERAL_GPIO_INPUT,
PERPIHERAL_GPIO_INPUT_PULLED_HIGH,
PERPIHERAL_GPIO_INPUT_PULLED_LOW,
PERPIHERAL_GPIO_OUTPUT_LOW,
PERPIHERAL_GPIO_OUTPUT_HIGH,
PERPIHERAL_EIC,
PERPIHERAL_EIC_PULLED_HIGH,
PERPIHERAL_EIC_PULLED_LOW,
PERPIHERAL_REF,
PERPIHERAL_ADC,
PERPIHERAL_AC,
PERPIHERAL_PTC,
PERPIHERAL_SERCOM_INPUT,
PERPIHERAL_SERCOM_OUTPUT,
PERPIHERAL_SERCOM_ALT_INPUT,
PERPIHERAL_SERCOM_ALT_OUTPUT,
PERPIHERAL_TC_E_OUTPUT,
PERPIHERAL_TC_E_INPUT,
PERPIHERAL_TC_F_OUTPUT,
PERPIHERAL_TC_F_INPUT,
PERPIHERAL_COM,
PERPIHERAL_AC_GCL,
}pinMuxType_t;
typedef struct {
uint32_t pinNum;
void *ptrPeriheral;
pinMuxType_t type;
uint32_t param; //pad pin waveform
pinMuxType_t sleepType;
}pin_t;

## Slide 7: Declaring a ‘Pin_t’
Const forces the structure to be in Flash memory only
  Means it can not change during execution
  Means it is not copied to SRAM either.
////Human/Machine interface connections for UART
#define PIN_HMI_TX((const pin_t){PIN_PA24, SERCOM3, PERPIHERAL_SERCOM_OUTPUT, PAD_2, PERPIHERAL_GPIO_INPUT_PULLED_LOW})
#define PIN_HMI_RX((const pin_t){PIN_PA25, SERCOM3, PERPIHERAL_SERCOM_INPUT, PAD_3, PERPIHERAL_GPIO_INPUT_PULLED_LOW})
typedef struct {
uint32_t pinNum;
void *ptrPeriheral;
pinMuxType_t type;
uint32_t param; //pad pin waveform
pinMuxType_t sleepType;
}pin_t;

## Slide 8: Using a Pin_t
Configure the pin
  PinConfig(PIN_HMI_TX)
Reading Pin
  PinRead(PIN_HMI_TX)
Writing Pin
  PinHigh(PIN_HMI_TX)
  PinLow(PIN_HMI_TX)

## Slide 9: Pin Abstraction for UART Driver
bool UartInit(uint32_t baud, pin_t tx, pin_t rx);
The pins are now parameters to the init function.
The correct SERCOM perpherial is part of the pins
We now can change pin assignments and not the code.

## Slide 10: To The Code

## Slide 11: Object Oriented Design
The pin struct is like a class (object)
Object oriented design can be done in C
  Inheritance
  Polymorphism
  Abstraction
  Encapsulation
Which of the above is provide with Pin_t?

## Slide 12: Class verse Struct
What if we made the Pin a class?
  PIN_HMI_TX.config();
  PIN_HMI_TX.high();
  PIN_HMI_TX.low();
  PIN_HMI_TX.read();
Is it cleaner?
  MEH?
Would/Could UART driver be cleaner as a Class?
  If so how?

## Slide 13: Object Oriented Design
Does not require C++
But why not use C++?
Where would C++ be better to use than C in embedded?